Clara Rockmore Theremin rebuild

I have built a ‘modern’ version of a Clara Rockmore Theremin, with the original RCA

# 27, #24, and the # 53 tubes. It was not easy to get the volume part working properly.

It took several coils and capacitor combinations before this part was working with normal sensitivity.

I started this project in 2003, but after my retirement in 2009 I started to take it seriously.

The start basics ware the hand drawn Rob Moog ‘Clara Rockmore’ schematics, the original RCA Theremin drawings and notes and other tube Theremin stuff from the Theremin ring.

The ‘Clara Rockmore’ Theremin with original tubes

Top view: see the modern battery’s two            1.5 V, AA and two 9V,  alkaline battery’s.

Cabinet front view

The power supply.

The original power supply tubes were difficult to get, here in the Netherlands.

I used a  European rectifier (RGU7Y) and as voltage regulator tubes  OC3 (105V - 40 mA).

Working in serial mode as in this supply: 30mA max.

The ‘Clara  Rockmore’  Theremin power supply.

The instrument is working very well.

Greetings from the Netherlands: Adrian Bontenbal

Email: a_bontenbal@live.nl